## Slide 1: Xilinx GPIO Interrupt example

## Slide 2: File->New Project

## Slide 3: Next

## Slide 4
Project name :
設定專案名稱
Project location:
設定專案路徑
Create project subdirectory:
設定專案路徑
設定完後按Next

## Slide 5: Select Project Type
不指定Sources
選擇RTL Project
選擇後按下一步

## Slide 6: Select your board
選擇Board->Zedbord Zynq Evaluation and Development Kit
選擇完畢後 Next

## Slide 8: IP INTEGRATOR Create Block Design

## Slide 10: Add IP

## Slide 11: Add PS(Processing system)

## Slide 12: Run block Automation

## Slide 13
確認完畢後按OK

## Slide 14: Add two GPIO IP

## Slide 15
兩個GPIO IP

## Slide 16: Setting IP connect

## Slide 17: Setting GPIO AXI
皆為Auto

## Slide 18: Setting GPIO
設定axi_gpio_0 GPIO Options Select Board Part Interface 為leds_8bits(LED)
設定axi_gpio_1 GPIO Options Select Board Part Interface 為btns_5bits(Puch buttons)
都設定完畢後按下OK

## Slide 19: axi_gpio_1 Enable Interrupt

## Slide 20: axi_gpio_1 Enable Interrupt

## Slide 21: Processing system Enable IRQ

## Slide 22: Processing system Enable IRQ

## Slide 23
將線路連接起來

## Slide 24: Regenerate layout

## Slide 25: Validation design

## Slide 26: Create HDL wrapper

## Slide 28: Generate Bitstream

## Slide 33: FileExportExport Hardware

## Slide 35: File Launch SDK

## Slide 37: FileNewapplication project

## Slide 38
設定專案名稱

## Slide 39
選擇Hello World Template

## Slide 40: Project Explore GPIO_Interrupt_testsrchelloworld.c
點兩下編輯

## Slide 41: Edit code
Reference:GPIO interrupt and processes (xilinx.com)
#include <stdio.h>
#include "platform.h“
#include "xparameters.h“
#include "xgpio.h“
#include "xscugic.h“
#include "xil_exception.h“
#include "xil_printf.h"
Include header file
#define INTC_DEVICE_ID XPAR_PS7_SCUGIC_0_DEVICE_ID
#define BTNS_DEVICE_ID XPAR_AXI_GPIO_1_DEVICE_ID
#define LEDS_DEVICE_ID XPAR_AXI_GPIO_0_DEVICE_ID
#define INTC_GPIO_INTERRUPT_ID XPAR_FABRIC_AXI_GPIO_1_IP2INTC_IRPT_INTR
#define BTN_INT XGPIO_IR_CH1_MASK
XGpio LEDInst, BTNInst;
XScuGic INTCInst;
static int led_data;
static int btn_value;
Parameter definitions

## Slide 42: Edit code
static void BTN_Intr_Handler(void *baseaddr_p);
static int InterruptSystemSetup(XScuGic *XScuGicInstancePtr);
static int IntcInitFunction(u16 DeviceId, XGpio *GpioInstancePtr);
PROTOTYPE FUNCTIONS

## Slide 43: Edit code
void BTN_Intr_Handler(void *InstancePtr) {
  // Disable GPIO interrupts
  XGpio_InterruptDisable(&BTNInst, BTN_INT);
  // Ignore additional button presses
  if ((XGpio_InterruptGetStatus(&BTNInst) & BTN_INT) != BTN_INT) {
  return;
  }
  btn_value = XGpio_DiscreteRead(&BTNInst, 1);
  // Increment counter based on button value
  // Reset if centre button pressed
  if (btn_value != 1)
  led_data = led_data + btn_value;
  else
  led_data = 0;
  XGpio_DiscreteWrite(&LEDInst, 1, led_data);
  (void) XGpio_InterruptClear(&BTNInst, BTN_INT);
  // Enable GPIO interrupts
  XGpio_InterruptEnable(&BTNInst, BTN_INT);
}
INTERRUPT HANDLER FUNCTIONS

## Slide 44: Edit code
int InterruptSystemSetup(XScuGic *XScuGicInstancePtr) {
  // Enable interrupt
  XGpio_InterruptEnable(&BTNInst, BTN_INT);
  XGpio_InterruptGlobalEnable(&BTNInst);
  Xil_ExceptionRegisterHandler(XIL_EXCEPTION_ID_INT,
  (Xil_ExceptionHandler) XScuGic_InterruptHandler,
  XScuGicInstancePtr);
  Xil_ExceptionEnable();
  return XST_SUCCESS;
}
INITIAL SETUP FUNCTIONS

## Slide 45
int IntcInitFunction(u16 DeviceId, XGpio *GpioInstancePtr) {
  XScuGic_Config *IntcConfig;
  int status;
  // Interrupt controller initialization
  IntcConfig = XScuGic_LookupConfig(DeviceId);
  status = XScuGic_CfgInitialize(&INTCInst, IntcConfig, IntcConfig->CpuBaseAddress);
  if (status != XST_SUCCESS)
  return XST_FAILURE;
  // Call to interrupt setup
  status = InterruptSystemSetup(&INTCInst);
  if (status != XST_SUCCESS)
  return XST_FAILURE;
  // Connect GPIO interrupt to handler
  status = XScuGic_Connect(&INTCInst, INTC_GPIO_INTERRUPT_ID,
  (Xil_ExceptionHandler) BTN_Intr_Handler, (void *) GpioInstancePtr);
  if (status != XST_SUCCESS)
  return XST_FAILURE;
  // Enable GPIO interrupts interrupt
  XGpio_InterruptEnable(GpioInstancePtr, 1);
  XGpio_InterruptGlobalEnable(GpioInstancePtr);
  // Enable GPIO and timer interrupts in the controller
  XScuGic_Enable(&INTCInst, INTC_GPIO_INTERRUPT_ID);
  return XST_SUCCESS;
}

## Slide 46
main
int main()
{
init_platform();
int status;
status = XGpio_Initialize(&LEDInst, LEDS_DEVICE_ID); // Initialise LEDs
if (status != XST_SUCCESS)
return XST_FAILURE;
status = XGpio_Initialize(&BTNInst, BTNS_DEVICE_ID); // Initialise Push Buttons
if (status != XST_SUCCESS)
return XST_FAILURE;
XGpio_SetDataDirection(&LEDInst, 1, 0x00); // Set LEDs direction to outputs
XGpio_SetDataDirection(&BTNInst, 1, 0xFF); // Set all buttons direction to inputs
status = IntcInitFunction(INTC_DEVICE_ID, &BTNInst); // Initialize interrupt controller
if (status != XST_SUCCESS)
return XST_FAILURE;
while (1);
cleanup_platform();
return 0;
}

## Slide 47: Program FPGA

## Slide 49: Run  Run As  Launch on Hardware(GDB)

## Slide 50
如果出現這種狀況到Run  Run configuration 修改成Reset Entire System

## Slide 51: Reference
Problem with ps7_init (xilinx.com)
Xilinx Zynq Vivado GPIO Interrupt Example – YouTube
GPIO interrupt and processes (xilinx.com)